## Slide 1: Lecture # 10 State diagram/sequence detector of mealy and Moore machine
By: Muhammad Zain Uddin
email: zuddin@iba.edu.pk

## Slide 2: The State Diagram
A state is an abstraction of memory
A state remembers a history of inputs applied to the circuit
Examples:
  State S0 represents the fact that the last input is a 0
  State S1 represents the fact that the last input is a 1
  State S2 represents the fact that the last two-input sequence is "11"
Obtaining the state diagram is the most important step
Requires experience and good understanding of the problem

## Slide 3: Example: Sequence Detector
A sequence detector is a sequential circuit
Detects a specific sequence of bits in the input
The input is a serial bit stream:
One input bit is fed to the sequence detector each cycle
The output is also a bit stream: One output bit each cycle
Indicates whether a given sequence is detected or not
Sequence Detector

## Slide 4: State Diagram for a Sequence Detector
S3
1
S2
1
S1
1
Example: Design a circuit that detects the input sequence "111"
Begin in an initial state: call it S0
S0 indicates that a 1 is NOT detected yet
As long as the input is 0, remain in the initial state S0
Add a state (call it S1) that detects the first 1 in the input
Add a state (call it S2) that detects the input sequence "11"
Add a state (call it S3) that detects the input sequence "111"
S0
0

## Slide 5: Complete the State Diagram
0
Moore Design: Assign Output to States
The output in S0, S1, and S2 should be 0
The output in S3 should be 1
0
0
S0
0
S1
0
S2
0
S3
1
1
1
1
0
1
Now complete the state diagram:
Add transitions from S1, S2, S3 back to S0 if the input is 0
Add transition from S3 to itself if the input is 1 to detect sequences longer than three 1's

## Slide 6: State Assignment
Each state must be assigned a unique binary code
If there are states, then
The minimum number of state bits:
is the smallest integer ≥ (ceiling function)
In our example, there are four states: S0, S1, S2, and S3
Therefore, the minimum number of state bits (Flip-Flops) = 2
State assignment: S0 = 00, S1 = 01, S2 = 10 and S3 = 11
If bits are used, the number of unused states =
In our example, there are NO unused states

## Slide 7: From State Diagram to State Table
0
0
0
S0
0
S1
0
S2
0
S3
1
1
1
1
0
1
Present State | Next State |  | Output
 | = 0 | = 1 | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S0 | S3 | 0
S3 | S0 | S3 | 1
Present State | Next State |  | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S0 | S3 | 0
S3 | S0 | S3 | 1
Present State | Next State |  | Output
 | = 0 | = 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
Present State | Next State |  | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
State Assignment
S0 = 00, S1 = 01
S2 = 10, S3 = 11

## Slide 8: Structure of a Moore Sequence Detector
In our design examples, only D-type Flip-Flops will be used
They are the simplest to analyze and implement
Next, we need minimal expressions for
Next State Logic
Output Logic
Next State
Logic
D Flip
Flops
Next
State
Current
State
Output
Logic
clock

## Slide 9: Derive Next State an Output Equations
Two D-type Flips-Flops
Present State = Flip-Flop Outputs and
Next State = Flip-Flop Inputs and
Next State equations: and
Output equation: (from the state diagram)
Present State | Next State |  | Output
 | = 0 | = 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
Present State | Next State |  | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
0
1
00
01
11
10
0
0
0
1
0
1
0
1
0
1
00
01
11
10
0
1
0
0
0
1
0
1

## Slide 10: Draw the Moore Sequence Detector Circuit
Output
Logic
Next State Logic
,

## Slide 11: Mealy Type Sequence Detector
Let us redesign a Mealy type "111" sequence detector
The initial state S0 indicates that a 1 is NOT detected yet
As long as the input is 0, remain in the initial state S0
Notice that input / output is written on the arc (Mealy type)
Add a state (call it S1) that detects the first 1 in the input
Add a state (call it S2) that detects the input sequence "11"
S0
0 / 0
1 / 0
S1
1 / 0
S2

## Slide 12: Complete the Mealy State Diagram
0 / 0
0 / 0
State S2 is reached after detecting the input sequence "11"
At S2, if the next input is 1 then the output should be 1
Make a transition from S2 back to itself labeled 1 / 1
No need for state S3, because output is on the arc
Now complete the state diagram
Add transitions from S1 and S2 back to S0 when input is 0
S0
0 / 0
1 / 0
S1
1 / 0
S2
1 / 1
Mealy Machines typically use
less states than Moore Machines

## Slide 13: State Assignment and State Table
Three States  Minimum number of state bits (Flip-Flops) = 2
Assign: S0 = 00, S1 = 01, and S2 = 10 (State 11 is Unused)
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
1 / 0
S2
1 / 1
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
S0 | S0 | S1 | 0 | 0
S1 | S0 | S2 | 0 | 0
S2 | S0 | S2 | 0 | 1
Present State | Next State |  |  | 
S0 | S0 | S1 | 0 | 0
S1 | S0 | S2 | 0 | 0
S2 | S0 | S2 | 0 | 1
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
Present State | Next State |  |  | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1

## Slide 14: Derive Next State and Output Equations
Present State = Flip-Flop Outputs and (state 11 is unused)
Next State = Flip-Flop Inputs and
Flip-Flop Input equations: and
Output equation:
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
1 1 | X X | X X | X | X
Present State | Next State |  |  | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
1 1 | X X | X X | X | X
0
1
00
01
11
10
0
0
0
1
X
X
0
1
0
1
00
01
11
10
0
1
0
0
X
X
0
0
0
1
00
01
11
10
0
0
0
0
X
X
0
1

## Slide 15: Draw the Mealy Sequence Detector Circuit
Reset
Output Logic
Next State
Logic
Next State
Logic

## Slide 16: Mealy versus Moore Sequence Detector
In general, Moore state diagrams have more states than corresponding Mealy.
The drawback of Mealy is that glitches can appear in the output if the input is not synchronized with the clock.
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
1 / 0
S2
1 / 1
0
0
0
S0
0
S1
0
S2
0
S3
1
1
1
1
0
1
Mealy Sequence Detector
Moore
Sequence
Detector

## Slide 17: Verification
Sequential circuits should be verified by showing that the circuit produces the original state diagram
Verification can be done manually, or with the help of a simulation program
All possible input combinations are applied at each state and the state variables and outputs are observed
A reset input is used to reset the circuit to its initial state
Apply a sequence of inputs to test all the state-input combinations, i.e., all transitions in the state diagram
Observe the output and the next state that appears after each clock edge in the timing diagram

## Slide 18: Input Test Sequence
Required to verify the correct operation of a sequential circuit
It should test each state transition of the state diagram
Test sequences can be produced from the state diagram
Consider the Mealy sequence detector, starting at S0 (reset), we can use an input test sequence to verify all state transitions:
Input test sequence: reset then x = 0, 1, 0, 1, 1, 0, 1, 1, 1, 1
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
reset
1 / 0
S2
1 / 1
Reset input forces initial state to be S0

## Slide 19: Verifying the Mealy Sequence Detector
Q0
Q1
S0
S0
S1
S0
S1
S2
S0
S1
S2
S2
Input test sequence: reset then x = 0, 1, 0, 1, 1, 0, 1, 1, 1, 1
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
reset
1 / 0
S2
1 / 1
z
reset
x
0
1
0
1
1
0
1
1
1
1
clock
cc0
cc1
cc2
cc3
cc4
cc5
cc6
cc7
cc8
cc9
cc10
0
0
0
0
0
0
0
0
1
1
glitch