## Slide 1: Lecture # 12 Counter logic /Ripple or Asynchronous counter/Synchronous counter/Integration of counter
By: Muhammad Zain Uddin
email: zuddin@iba.edu.pk

## Slide 2: Counter
Sequential circuit that goes through a specific sequence of states
Output of the counter is the count value
Modulo-N counter: goes through 0, 1, 2, …, (N – 1)
Modulo-8 binary counter goes through 0, 1, 2, …, 7
Modulo-10 (BCD) counter goes through 0, 1, 2, …, 9
Counting can be up or down
Some Applications:
  Timers
  Event Counting
  Frequency Division
Counter
n

## Slide 3: Implementing Counters
Two Basic Approaches:
Ripple Counters
  The system clock is connected to the clock input of the first flip-flop (LSB)
  Each flip-flop output connects to the clock input of the next flip-flop
  Advantage: simple circuit and low power consumption
  Disadvantage: The counter is not truly synchronous
  No common clock to all flip-flops
  Ripple propagation delay as the clock signal propagates to the MSB
Synchronous Counters
  The system clock is connected to the clock input of ALL flip-flops
  Combinational logic is used to implement the desired state sequence

## Slide 4: Ripple Counter
Q0 toggles at the positive edge of every cycle
Q1 toggles when Q0 goes from 1 down to 0
Q2 toggles when Q1 goes from 1 down to 0
Q3 toggles when Q2 goes from 1 down to 0
Q3 | Q2 | Q1 | Q0
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
Counts Up from 0 to 15 then back to 0

## Slide 5: Ripple Counter (cont'd)
Up Count |  |  |  | Down Count |  |  | 
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
Up Count |  |  |  | Down Count |  |  | 
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
is the Up Count
is the Down Count
Connect
Q0 to Clk Q1 Q1 to Clk Q2
Q2 to Clk Q3
How to Count
Down?

## Slide 6: Timing of a Ripple Counter
Drawback of ripple counter:
Flip-flops are NOT driven by the same clock (Not Synchronous)
Q delay increases as we go from Q0 to Q3
Given  = flip-flop delay  Delay of Q0, Q1, Q2, Q3 = , 2, 3, 4
Clock
Q0
Q1
Q2
Q3

## Slide 7: Synchronous Counter
Avoid clock rippling
-bit Register with a common clock for all flip-flops
-bit Incrementer to generate next state (Up-Counter)
n-bit Register
n-bit Incrementer (+1)

## Slide 8: 4-Bit Synchronous Counter with Enable
4-Bit Incrementer
An incrementer is a reduced (contracted) form of an adder
4-bit Counter Output
EN = 0 
No Change
EN = 1 
Increment
How to
Count
Down?
Increment
Q' (Not Q)

## Slide 9: Synchronous Counter (Counting Up)
Count Up
When = 1
Toggle (Complement)
When = = 1
Toggle (Complement)
When = = = 1
Toggle (Complement)
Count Up |  |  | 
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1
Count Up |  |  | 
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1

## Slide 10: 4-Bit Synchronous Counter with T Flip-Flops
Toggle Q1 when c1 = 1, Toggle Q2 when c2 = 1, etc.
EN = 0 
No Change
EN = 1 
Increment
4-bit Counter Output

## Slide 11: Synchronous Up-Down Counter (T Flip-Flops)
Count Down
When = 0
Toggle
When = = 0
Toggle
When = = = 0
Toggle
Count Down |  |  | 
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1
Count Down |  |  | 
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1

## Slide 12: Timing of a Synchronous Counter
Advantage of Synchronous counter:
ALL Flip-flops are driven by the same clock
Delay of all outputs is identical  Delay of Q0 = Q1 = Q2 = Q3 = 
Clock
Q0
Q1
Q2
Q3

## Slide 13: Frequency Division
A counter can be used as a frequency divider
Counter is driven by a Clock with frequency F
Output Q0 Frequency = F/2, Output Q1 Frequency = F/4
Output Q2 Frequency = F/8, Output Q3 Frequency = F/16
Clock
Q0
Q1
Q2
Q3

## Slide 14: BCD Counter
Problem: Convert a 4-bit binary counter into a BCD counter
Solution: When output reaches 9 then reset back to 0
Asynchronous Reset: Count to 10 and reset immediately
4-bit Counter with
Synchronous Reset
4-bit
Counter
1
(Synchronous)
4-bit Counter with
Asynchronous Reset
4-bit
Counter
1
(Asynchronous)

## Slide 15: Building Larger Synchronous Counters
Smaller counters can be used to build a larger counter
Example: 12-bit counter designed using three 4-bit counters
Counts from 0 to 4095 (212 – 1), then back to 0
The of a 4-bit counter is used to enable the next counter
4-bit
Counter
4
4-bit
Counter
4
4-bit
Counter
4

## Slide 16: Synchronous Counter with Parallel Load
Ability to load an initial binary number into the counter
  Prior to the count operation
Two control inputs:
  Load: Initialize counter with input Data
  EN: enables the counting
4-bit
Counter
4
4
Very useful in implementing different counting sequences

## Slide 17: Implementing a Counter with Parallel Load
4-bit Counter Output
1
0
1
0
1
0
1
0
Load | EN | Action
0 | 0 | No change
0 | 1 | Increment Count
1 | X | Load data

## Slide 18: 3-to-12 Counter
Convert a 4-bit binary counter with load into 3-to-12 counter
Solution: Detect binary count 12 and then load 3
Detect 12: Binary count with Q3 = Q2 = 1
4-bit Counter
0
0
1
1
Synchronous Preset
Load: 0011

## Slide 19: 9-to-99 Counter
Problem: Use two 4-bit binary counters with parallel load and logic gates to build a counter that counts from 9 to 99 = 'b01100011
Add a synchronous Preset input to initialize the counter to value 9
4-bit Counter
4-bit Counter
0
1
0
0
1