## Slide 1: Lecture # 3 Introduction to Boolean algebra/Types of input/ Logic gates/
By: Muhammad Zain Uddin
email: zuddin@iba.edu.pk

## Slide 2: Digital Logic Design
Muhammad Zain Uddin
Lecturer,
IBA

## Slide 3: Review of previous lecture
Different types of input
Logic gate representation
Designing rule
Boolean Algebra
SOP and POS

## Slide 4: Boolean Addition
In Boolean algebra, a variable is a symbol used to represent an action, a condition, or data. A single variable can only have a value of 1 or 0.
The complement represents the inverse of a variable and is indicated with an overbar. Thus, the complement of A is A.
A literal is a variable or its complement.
Addition is equivalent to the OR operation. The sum term is 1 if one or more if the literals are 1. The sum term is zero only if each literal is 0.
Determine the values of A, B, and C that make the sum term of the expression A + B + C = 0?
Each literal must = 0; therefore A = 1, B = 0 and C = 1.

## Slide 5: Boolean Multiplication
In Boolean algebra, multiplication is equivalent to the AND operation. The product of literals forms a product term. The product term will be 1 only if all of the literals are 1.
What are the values of the A, B and C if the product term of A.B.C = 1?
Each literal must = 1; therefore A = 1, B = 0 and C = 0.

## Slide 6: Commutative Laws
In terms of the result, the order in which variables are ORed makes no difference.
The commutative laws are applied to addition and multiplication. For addition, the commutative law states
A + B = B + A
In terms of the result, the order in which variables are ANDed makes no difference.
For multiplication, the commutative law states
AB = BA

## Slide 7: Associative Laws
When ORing more than two variables, the result is the same regardless of the grouping of the variables.
The associative laws are also applied to addition and multiplication. For addition, the associative law states
A + (B +C) = (A + B) + C
For multiplication, the associative law states
When ANDing more than two variables, the result is the same regardless of the grouping of the variables.
A(BC) = (AB)C

## Slide 8: Distributive Law
The distributive law is the factoring law. A common variable can be factored from an expression just as in ordinary algebra. That is
AB + AC = A(B+ C)
The distributive law can be illustrated with equivalent circuits:
AB + AC
A(B+ C)

## Slide 9: Rules of Boolean Algebra
1. A + 0 = A
2. A + 1 = 1
3. A . 0 = 0
4. A . 1 = A
5. A + A = A
7. A . A = A
6. A + A = 1
8. A . A = 0
9. A = A
=
10. A + AB = A
12. (A + B)(A + C) = A + BC
11. A + AB = A + B

## Slide 10: Rules of Boolean Algebra
Rules of Boolean algebra can be illustrated with Venn diagrams. The variable A is shown as an area.
The rule A + AB = A can be illustrated easily with a diagram. Add an overlapping area to represent the variable B.
The overlap region between A and B represents AB.
The diagram visually shows that A + AB = A. Other rules can be illustrated with the diagrams as well.
=

## Slide 11: Rules of Boolean Algebra
Rule 12, which states that (A + B)(A + C) = A + BC, can be proven by applying earlier rules as follows:
(A + B)(A + C) = AA + AC + AB + BC
= A + AC + AB + BC
= A(1 + C + B) + BC
= A . 1 + BC
= A + BC
This rule is a little more complicated, but it can also be shown with a Venn diagram, as given on the following slide…

## Slide 12
The area representing A + B is shown in yellow.
The area representing A + C is shown in red.
Three areas represent the variables A, B, and C.
The overlap of red and yellow is shown in orange.
ORing with A gives the same area as before.
=
(A + B)(A + C)
A + BC
The overlapping area between B and C represents BC.

## Slide 13: DeMorgan’s Theorem
The complement of a product of variables is equal to the sum of the complemented variables.
DeMorgan’s 1st Theorem
AB = A + B
Applying DeMorgan’s first theorem to gates:

## Slide 14: DeMorgan’s Theorem
DeMorgan’s 2nd Theorem
The complement of a sum of variables is equal to the product of the complemented variables.
A + B = A . B
Applying DeMorgan’s second theorem to gates:

## Slide 15: Summary of Laws

## Slide 16: Boolean Analysis of Logic Circuits
Combinational logic circuits can be analyzed by writing the expression for each gate and combining the expressions according to the rules for Boolean algebra.
Apply Boolean algebra to derive the expression for X.
Write the expression for each gate:
Applying DeMorgan’s theorem and the distribution law:
C (A + B )
= C (A + B )+ D
(A + B )
X = C (A B) + D = A B C + D
X

## Slide 17: Combinational Logic Circuits
In Sum-of-Products (SOP) form, basic combinational circuits can be directly implemented with AND-OR combinations if the necessary complement terms are available.

## Slide 18: Combinational Logic Circuits
An example of an SOP implementation is shown. The SOP expression is an AND-OR combination of the input variables and the appropriate complements.
SOP
DE
ABC
A
B
C
E
D
X = ABC
+ DE

## Slide 19: Combinational Logic Circuits
When the output of a SOP form is inverted, the circuit is called an AND-OR-Invert circuit. The AOI configuration lends itself to product-of-sums (POS) implementation.
An example of an AOI implementation is shown. The output expression can be changed to a POS expression by applying DeMorgan’s theorem twice.
POS
DE
ABC
A
B
C
E
D
X = ABC
+ DE
X = ABC
+ DE
X = (A + B + C)(D + E)
X = (ABC)(DE)
AOI
DeMorgan

## Slide 20: Exclusive-OR Logic
The truth table for an exclusive-OR gate is
A
B
Notice that the output is HIGH whenever A and B disagree.
The Boolean expression is
The circuit can be drawn as
X
Symbols:
Distinctive shape Rectangular outline
X = AB + AB

## Slide 21: Exclusive-NOR Logic
The truth table for an exclusive-NOR gate is
A
B
Notice that the output is HIGH whenever A and B agree.
The Boolean expression is
The circuit can be drawn as
X
Symbols:
Distinctive shape Rectangular outline
X = AB + AB

## Slide 22: Basic Designing Rules
Step 1: identify number of inputs and individual input bits
Step 2: draw truth table if total number of inputs bits
Step 3: identify number of outputs and output bits
Step 4: Identify output value on each combination of inputs
:
Step 6: Now determine Boolean expression of each output bit.
Step 7 : Simplify this equation using Boolean rules laws or Kmap
Step 8: Draw the circuit diagram of that simplified equation.

## Slide 23: To understand Step 5 lets take an Example
A2 | A1 | A0 | X2 | X1 | X0
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0

## Slide 24: Solution continue
Before analyzing Boolean expression of output do you think there is any relationship of invidual output will all inputs or single input bit….
If you look closely you will find,
X0 is inverse of A0
X1 is XOR of A2,A1,A0
So now we can conclude our rules
A2 | A1 | A0 | X2 | X1 | X0
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0

## Slide 25: Basic Designing Rules
Step 1: identify number of inputs and individual input bits
Step 2: draw truth table if total number of inputs bits
Step 3: identify number of outputs and output bits
Step 4: Identify output value on each combination of inputs
Step 5: identify whether any output can be solve using single gate or related to single or multiple inputs.
Step 6: Now determine Boolean expression of each output bit.
Step 7 : Simplify this equation using Boolean rules laws or Kmap
Step 8: Draw the circuit diagram of that simplified equation.