## Slide 1: Lecture # 6 Arithmetic of Boolean algebra/Half adder/Full Adder/Parallel Adder/Comparator
By: Muhammad Zain Uddin
email: zuddin@iba.edu.pk

## Slide 2: Digital Logic Design
Muhammad Zain Uddin
Lecturer,
IBA

## Slide 3: Review of previous lecture
5 inputs K-map
3,4 and 5 inputs K map examples
Function of Boolean Algebra
Decoder Designing (Binary to Deimal, BCD to Decimal etc)
Encoder Designing (Decimal to binary, Decimal to BCD etc)

## Slide 4: Full-Adder
By contrast, a full adder has three binary inputs (A, B, and Carry in) and two binary outputs (Carry out and Sum). The truth table summarizes the operation.
A full-adder can be constructed from two half adders as shown:
A
B
S
Cout
S
A
B
S
Cout
S
A
B
Sum
Cout
Cin
A
B
S
Cout
S
Cin
Symbol

## Slide 5: Full-Adder
A
B
S
Cout
S
A
B
S
Cout
S
Example
Solution
For the given inputs, determine the intermediate and final outputs of the full adder.
1
1
0
1
0
The first half-adder has inputs of 1 and 0; therefore, the Sum =1 and the Carry out = 0.
The second half-adder has inputs of 1 and 1; therefore, the Sum = 0 and the Carry out = 1.
The OR gate has inputs of 1 and 0, therefore the final carry out = 1.
1
0
1
Sum
Cout

## Slide 6: Full-Adder
A
B
S
Cout
S
A
B
S
Cout
S
1
1
0
1
0
1
0
1
Sum
Cout
Notice that the result from the previous example can be read directly on the truth table for a full adder.

## Slide 7: Parallel Adders
Full adders are combined into parallel adders that can add binary numbers with multiple bits. A 4-bit adder is shown.
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A1 B1
S1
C0
S2
S3
S4
C1
C2
C3
C4
A2 B2
A3 B3
A4 B4
The output carry (C4) is not ready until it propagates through all of the full adders. This is called ripple carry, delaying the addition process.

## Slide 8: Parallel Adders
The logic symbol for a 4-bit parallel adder is shown. This 4-bit adder includes a carry in (labeled (C0) and a Carry out (labeled C4).
The 74LS283 is an example. It features look-ahead carry, which adds logic to minimize the output carry delay. For the 74LS283, the maximum delay to the output carry is 17 ns.
Binary number A
Binary number B
Input carry
4-bit sum
Output carry
1
2
3
4
1
2
3
4
1
2
3
4
C0
C4
S

## Slide 9: Half- Subtractor Function Table
Input |  | Output | 
A | B | Diff | Bor
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0

## Slide 10: Full-Subtractor Function Table
Input |  |  | Output | 
A | B | C | Diff | Bor
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
A’B’
A’B
AB
A’B
1
1
1
1
C’
C

## Slide 11: 4-bit Parallel Subtractor

## Slide 12
A complete logical circuit capable of adding or subtracting two numbers by using 2’s complement is shown in Figure below
Binary Adder and Subtractor

## Slide 13: Integration of multiple fuction

## Slide 14: Adding Multiple inputs of multiple bits
In Situation like this when you know you can’t design using single function so analyze how many and which type of adder function you need ? You have following function
    Half adder(can add two inputs of one bit each and produce an output of two bits)
    Full Adder(can add three inputs of one bit each and produce an output of two bits)
    Parallel adder (can add two inputs of four bits each and produce an output of five bits)
  Now if you are adding more than two inputs having multiple bits it is suggested to use parallel adder as parallel adder can add multiple bits two inputs easily
  But if you are adding single bit input you can use half and full adder with parallel adder easily

## Slide 15: Comparators
The function of a comparator is to compare the magnitudes of two binary numbers to determine the relationship between them. In the simplest form, a comparator can test for equality using XNOR gates.
Example
Solution
How could you test two 4-bit numbers for equality?
AND the outputs of four XNOR gates.
A1
B1
A2
B2
A3
B3
A4
B4
Output

## Slide 16: Comparators
IC comparators provide outputs to indicate which of the numbers is larger or if they are equal. The bits are numbered starting at 0, rather than 1 as in the case of adders. Cascading inputs are provided to expand the comparator to larger numbers.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
Cascading inputs
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
The IC shown is the 4-bit 74LS85.

## Slide 17: Comparators
IC comparators can be expanded using the cascading inputs as shown. The lowest order comparator has a HIGH on the A = B input.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
A5
A4
A6
A7
B5
B4
B6
B7
+5.0 V
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
LSBs
MSBs