## Slide 1: Lecture # 7 Comparator/Mux-Demux/Designing through mux/Integration of Functions
By: Muhammad Zain Uddin
email: zuddin@iba.edu.pk

## Slide 2: Digital Logic Design
Muhammad Zain Uddin
Lecturer,
IBA

## Slide 3: Review of previous lecture
Cascading of functions
Adder (Half, Full, Parallel)
Athematic using adder function
Subtractor (Half Full)
Adder Subtractor
Comparator (Con.t)

## Slide 4: Comparators
The function of a comparator is to compare the magnitudes of two binary numbers to determine the relationship between them. In the simplest form, a comparator can test for equality using XNOR gates.
Example
Solution
How could you test two 4-bit numbers for equality?
AND the outputs of four XNOR gates.
A1
B1
A2
B2
A3
B3
A4
B4
Output

## Slide 5: Comparators
IC comparators provide outputs to indicate which of the numbers is larger or if they are equal. The bits are numbered starting at 0, rather than 1 as in the case of adders. Cascading inputs are provided to expand the comparator to larger numbers.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
Cascading inputs
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
The IC shown is the 4-bit 74LS85.

## Slide 6: Comparators
IC comparators can be expanded using the cascading inputs as shown. The lowest order comparator has a HIGH on the A = B input.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
A5
A4
A6
A7
B5
B4
B6
B7
+5.0 V
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
LSBs
MSBs

## Slide 7: Multiplexer (Data Selectors)
The term Multiplexer means many into one.
Multiplexing is the process of transmitting a large number of information over a single line.
A Digital Multiplexer (MUX) is a combinational Circuit that select one digital information from several sources and transmits the selected information on a single output line.
A Multiplexer is also called a Data Selector.
The Multiplexer has several data input line and a single output line.

## Slide 8: Mux (Con.t)
MUX directs one of the inputs to its output line by using a control bit word (selection line) to its select lines.
Multiplexer contains the followings:
data inputs
selection inputs
a single output
Selection input determines the input that should be connected to the output.
The multiplexer acts like an electronic switch that selects one from different.

## Slide 16
8-1 Multiplexer Circuit

## Slide 17: De-Multiplexer
The De-Multiplexer is a combinational logic circuit that performs the reverse operation of multiplexer (Several output lines, one input line).
De -Multiplexer means one to many. A De-Multiplexer is a circuit with one input and many output. By applying control signal, we can steer any input to the output. Few types of De -Multiplexer are 1-to 2, 1-to-4, 1-to-8 and 1-to 16 De -Multiplexer .
De-Multiplexer is the process of taking information from one input and transmitting the same over one of several outputs.

## Slide 21: Switching-network logic blocks
Multiplexer (MUX)
  Routes one of many inputs to a single output
  Also called a selector
Demultiplexer (DEMUX)
  Routes a single input to one of many outputs
  Also called a decoder
multiplexer
demultiplexer
control
control
We construct these
devices from:
logic gates
networks of tran-
sistor switches

## Slide 22: The “WHY” slide
Multiplexers/Demultiplexers
  If you had the ability to select which input to operate, the same part of a circuit can be used multiple times. So if you have a lot of inputs and all of them are supposed to go through same complex logic functions, you can save a lot of space on your circuit board by using a multiplexer.
  Then you will also need a demultiplexer to decode the output coming out in serial into separate output ports.

## Slide 23: “WHY”: Sharing complex logic functions
Share an adder: Select inputs; route sum
multiple inputs
multiple output destinations
MUX
A
B
Sum
A0 A1
Ss
Sb
B0 B1
MUX
DEMUX
Z0 Z1
single adder
Sa

## Slide 24: Multiplexers (con't)
2:1 mux: Z = S'In0 + SIn1
4:1 mux: Z = S0'S1'In0 + S0'S1In1 + S0S1'In2 + S0S1In3
8:1 mux: Z = S0'S1'S2'In0 + S0'S1S2In1 + ...
I0 I1 I2 I3 I4 I5 I6 I7
S0 S1 S2
8:1 mux
Z
I0 I1 I2 I3
S0 S1
4:1 mux
Z
I0 I1
S0
2:1 mux
Z

## Slide 25: Cascading multiplexers
Can form large multiplexers from smaller ones
  Many implementation options
Z
4:1 mux
S2
2:1 mux
I4 I5 I6 I7
S0 S1
4:1 mux
S0
Z
S1 S2
4:1 mux
2:1 mux
2:1 mux
2:1 mux
2:1 mux
I4 I5
I2 I3
I0 I1
I6 I7
8:1 mux
8:1 mux
I0 I1 I2 I3

## Slide 26: Multiplexers as general-purpose logic
A 2n:1 mux can implement any function of n variables
  A lookup table
  A 2n – 1:1 mux also can implement any function of n variables
Example: F(A,B,C) = m0 + m2 + m6 + m7 = A'B'C' + A'BC' + ABC' + ABC = A'B'(C') + A'B(C') + AB()
A B C F 0 0 0 1 0 0 1 0 0 1 0 1 0 1 1 0 1 0 0 0 1 0 1 0 1 1 0 1 1 1 1 1
C' C' 0 1
S1
S0
F
0 1 2 3
4:1 MUX
C' C' 0 1
0 1 2 3 4 5 6 7
1 0 1 0 0 0 1 1
S2
8:1 MUX
S1
S0
F
A B C
A B

## Slide 27: Multiplexers as general-purpose logic

## Slide 28: Multiplexers as general-purpose logic

## Slide 29: Multiplexers as general-purpose logic